## Slide 1: CS 2160 Introduction to Assembly Programming and Computer Organization Lecture 07: Instruction Representations
Fall 2026
Instructor: Himon Thakur
TA: Hassan Shakil
University of Colorado Colorado Springs (UCCS)
Himon Thakur (hthakur@uccs.edu); CC BY-NC-SA 4.0;
Special Thanks to Dr. Keith Paarpong and Dr. Xi Tan.

## Slide 2: Today’s Agenda.
Understand how instructions are represented
PC-relative addressing
Strings

## Slide 3: RISK-V Integer Instructions.
Name | Mnemonic | Meaning
x0 | zero | always zero
x1 | ra | return address
x2 | sp | stack pointer
x3 | gp | global pointer
x4 | tp | thread pointer
x5 | t0 | temporary (alternate return address)
x6-7 | t1-2 | temporary registers
x8 | s0/fp | saved register / frame pointer
x9 | s1 | saved register
x10-11 | a0-1 | function arguments and return value
x12-17 | a2-7 | function arguments
x18-27 | s2-11 | saved registers
x28-31 | t3-6 | temporary registers

## Slide 4: What Data Means.
What does this piece of data represent?
1000 0010 0000 0100 0000 1100 0110 0011

## Slide 5: What Data Means.
It depends on the data representation and context.
- Integer? Floating point?
- Alphanumeric character?
- A machine instruction?
- Other?
What does this piece of data represent?
1000 0010 0000 0100 0000 1100 0110 0011

## Slide 6
American Standard Code for Information Interchange (ASCII)
- Encode alpha-numeric symbols with 7 bits.
- Store in 8 bits, upper bit is reserved
- Can represent 128 characters.
Humans Need Characters and Strings.

## Slide 7: Each character represented with 8 bits (a byte)
0: Null character (marks the end of a string)
ASCII.

## Slide 8
void strcpy(char x[], char y[])
{
int i = 0;
while ((x[i]=y[i]) != ‘\0’) i += 1;
}
Copy string y into string x
String Example.

## Slide 9
Assume base &x[0] and &y[0] are contained in the a0 and a1 registers, and I is contained in s3.
String Example.
// save register value
// initialize i to 0
strcpy:
addi sp, sp, -4 sw s2, 0(sp) add s2, x0, x0
L1:
add | t0, | s2, | a1 | // | t0 | <- | addr | of | y[i]
lbu | t1, | 0(t0) |  | // | t1 | = y[i] |  |  | 
add | t2, | s2, a0 |  | // | t2 | <- addr |  | of | x[i]
sb t1, 0(t2) beq t1, x0, L2 addi s2, s2, 1 jal x0, L1 |  |  |  | // // | x[i] exit |  | = y[i] if y[i] |  | = NULL
L2:
lw s2, 0(sp) addi sp, sp, 4 jalr x0, 0(ra)

## Slide 10
Instructions are represented by numbers
add x9, x20, x21
This instruction is represented by the decimal numbers
What do these numbers mean?
Instruction Representation.

## Slide 11
Instructions are represented by numbers
add x9, x20, x21
This instruction is represented by the decimal numbers
Instruction Representation.
opcode fields
Each segment is a field

## Slide 12
Instructions are represented by numbers
add x9, x20, x21
This instruction is represented by the decimal numbers
Instruction Representation.
Each segment is a field
Source registers
Destination register

## Slide 13
Instructions are represented by numbers
add x9, x20, x21
Binary representation of this instruction:
Instruction Representation.
This layout is called an instruction format
ALL RISC-V instructions are 32 bits long

## Slide 14
Opcode: basic operation of the instruction
rd: destination register
rs1: first source register
rs2: second source register
funct7: another opcode field
funct3: another opcode field
RISC-V Fields.

## Slide 15
RISC-V Fields.
This is an R-type RISC-V instruction (add, sub)
We cannot describe immediate
type instructions (addi, lw, slli) with this format

## Slide 16
Opcode: basic operation of the instruction
rd: destination register
rs1: source register
immediate: a value in two’s complement
funct3: another opcode field
This is an I-type RISC-V instruction (addi, lw, slli)
RISC-V Fields.

## Slide 17
Example:
This is an I-type RISC-V instruction (addi, lw, slli)
lw x9, 32(x22)
What about store instructions?
RISC-V Fields.

## Slide 18
This is an S-type RISC-V instruction (sw, sb)
RISC-V Fields.

## Slide 19
I-type instructions only handle 12-bit immediate field
2^12 = 4096.
This is a tiny number!
The load immediate (li) pseudoinstruction should be able to load any 32-bit value into a register.
Instructions with Wide Immediate.

## Slide 20
Example: Load the constant 3,998,976 into register x19
Instructions with Wide Immediate.

## Slide 21
Example: Load the constant 3,998,976 into register x19
Instructions with Wide Immediate.

## Slide 22
Example: Load the constant 3,998,976 into register x19
00000000 00111101 00000101 00000000
Instructions with Wide Immediate.

## Slide 23
Example: Load the constant 3,998,976 into register x19
00000000 00111101 00000101 00000000
Instructions with Wide Immediate.
First, load the upper 20 bits with load upper immediate
lui x19, 976 // 976 = 0000 0000 0011 1101 0000
// x19 has 00000000 00111101 00000000 00000000

## Slide 24
Example: Load the constant 3,998,976 into register x19
00000000 00111101 00000101 00000000
Instructions with Wide Immediate.
First, load the upper 20 bits with load upper immediate
lui x19, 976 // 976 = 0000 0000 0011 1101 0000
// x19 has 00000000 00111101 00000000 00000000
Then, add in the least significant 12 bits
addi x19, x19, 1280 // 1280 = 00000101 00000000
// x19 has 00000000 00111101 00000101 00000000

## Slide 25
This is a U-type instruction
Instructions with Wide Immediate.

## Slide 26
jal x0, 2000 // goto location 0111 1101 0000
This could be represented by a UJ-type instruction,
But 20 bits is far too small to specify all addresses!
Instead, one can use PC-relative addressing
Program Counter = Program Counter + Branch offset
How Are Branch Instructions Encoded?

## Slide 27
Example: Branch offsets in machine language
Loop:
slli x10, x22, 2 add x10, x10, x25 lw x9, 0(x10)
bne x9, x24, Exit addi x22, x22, 1 beq x0, x0, Loop
Exit:
Conditional branches are SB-type instructions
How Are Branch Instructions Encoded?

## Slide 28
Example: Branch offsets in machine language
Loop:
slli x10, x22, 2 add x10, x10, x25 lw x9, 0(x10)
bne x9, x24, Exit addi x22, x22, 1
beq x0, x0, Loop
Exit:
imm[11:5]
rs2 rs1
imm[4:0] "goto PC + 12”
How Are Branch Instructions Encoded?

## Slide 29
Example: Branch offsets in machine language
Loop:
slli x10, x22, 2 add x10, x10, x25 lw x9, 0(x10)
bne x9, x24, Exit addi x22, x22, 1 beq x0, x0, Loop
Exit:
imm[11:5]
rs2 rs1
imm[4:0]
"goto PC - 20”
How Are Branch Instructions Encoded?