## Slide 1: CS 2160 Introduction to Assembly Programming and Computer Organization Lecture 04: Logical Operations
Fall 2026
Instructor: Himon Thakur
TA: Hassan Shakil
University of Colorado Colorado Springs (UCCS)
Himon Thakur (hthakur@uccs.edu); CC BY-NC-SA 4.0;
Special Thanks to Dr. Keith Paarpong and Dr. Xi Tan.

## Slide 2: Today’s Agenda.
Understand RISC-V basic Assembly logical and arihtmetic operations.
Signed and unsigned numbers
1's and 2's complement

## Slide 3: Unsigned Binary Integers (§ 2.4)
Given an n-bit number, xi = 0 or 1
Range: 0 to +2n – 1
Example
  0000 0000 … 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110

## Slide 4: 2s-Complement Signed Integers
Given an n-bit number, xi = 0 or 1
Range: –2n – 1 to +2n – 1 – 1
Example
  1111 1111 … 1111 11002 = –1×231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410

## Slide 5: 2s-Complement Signed Integers
Bit 31 is sign bit
  1 for negative numbers
  0 for non-negative numbers
–(–2n – 1) can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111

## Slide 6: Signed Negation
Complement and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 0010two
  –2 = 1111 1111 … 1101two + 1 = 1111 1111 … 1110two

## Slide 7: Sign Extension
Representing a number using more bits
  Preserve the numeric value
Replicate the sign bit to the left
  c.f. unsigned values: extend with 0s
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110
In RISC-V instruction set
  lb: sign-extend loaded byte
  lbu: zero-extend loaded byte

## Slide 8: Logical Operations (§2.6 )
Operate on fields of bits within a word or even on individual bits
Operation | C | Java | RISC-V
Shift left logical | << | << | sll, slli
Shift right logical | >> | >>> | srl, srli
Shift right arithmetic | >> | >> | sra, srai
Bit-by-bit AND | & | & | and, andi
Bit-by-bit OR | ¦ | ¦ | or, ori
Bit-by-bit XOR | ^ | ^ | xor, xori
Bit-by-bit NOT | ~ | ~ | xori
Table: C and Java logical operators and their corresponding RISC-V instructions

## Slide 9: Shift Operations
immed: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  slli by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srli by i bits divides by 2i (unsigned only)
rs1
rd
funct3
opcode
6 bits
7 bits
5 bits
5 bits
3 bits
funct6
immed
6 bits

## Slide 10: Shift Operations – shift left/right logical
move all the bits in a doubleword to the left or right, filling the emptied bits with 0s
Example: x19 has a value of 9
00000000 00000000 00000000 00000000 00000000 00000000 00000000 00001001two = 9ten
slli x11, x19, 4
00000000 00000000 00000000 00000000 00000000 00000000 00000000 10010000two = 144ten
Notes: Our discussion today aims to continue your orientation toward understanding and writing assembly source code for the RISC-V ISA.

## Slide 11: Shift Operations – shift right arithmetic
it fills the vacated bits on the left with copies of the old sign bit
Example: x19 has a value of -9
srai x11, x19, 4
00000000 00000000 00000000 00000000 00000000 00000000 00000000 10010000two = 144ten
Notes: Our discussion today aims to continue your orientation toward understanding and writing assembly source code for the RISC-V ISA.

## Slide 12: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and x9,x10,x11
00000000 00000000 00000000 00000000 00000000 00000000 00001101 11000000
x10
x11
x9
00000000 00000000 00000000 00000000 00000000 00000000 00111100 00000000
00000000 00000000 00000000 00000000 00000000 00000000 00001100 00000000

## Slide 13: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or x9,x10,x11
00000000 00000000 00000000 00000000 00000000 00000000 00001101 11000000
x10
x11
x9
00000000 00000000 00000000 00000000 00000000 00000000 00111100 00000000
00000000 00000000 00000000 00000000 00000000 00000000 00111101 11000000

## Slide 14: XOR Operations
Differencing operation
  Set some bits to 1, leave others unchanged
xor x9,x10,x12 // NOT operation
00000000 00000000 00000000 00000000 00000000 00000000 00001101 11000000
x10
x12
x9
11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
11111111 11111111 11111111 11111111 11111111 11111111 11110010 00111111

## Slide 15: Summary: Some Arithmetic Operations
Carnegie Mellon
  Format Computation
    add Dest, Src1, Src2 Dest = Src1 + Src2
    sub Dest, Src1, Src2 Dest = Src1  Src2
    sll Dest, Src1, Src2 Dest = Src1 << Src2 Inserts 0 in the lsb
    sra Dest, Src1, Src2 Dest = Src1 >> Src2 Shift arithmetic preserves sign bit
    srl Dest, Src1, Src2 Dest = Src1 >> Src2 Shift logical adds 0 bit in the msb
    xor Dest, Src1, Src2 Dest = Dest ^ Src
    and Dest, Src1, Src2 Dest = Dest & Src
    or Dest, Src1, Src2 Dest = Dest | Src
  These are all available with immediate versions (except sub):
  addi Dest, Src1, Imm Dest = Src1 + Imm
Notes: Here are some of the most commonly used arithmetic-logic operations. They take either two source registers or a source register and a signed 12-bit immediate value. The add instruction calculates the value of the source 1 register plus the source 2 register, and puts the result in the destination register. This is the same in all the arithmetic instructions. Noticeably absent is multiplication, which we may revisit later. Sll is shift left logical, which bit shifts the source 1 operand left by the number of spaces specified by source 2, filling with zeroes from the right. Likewise, shift arithmetic right does a right-shift of dest by the number of bits specified in the source, but it fills in from the left with whatever value the most significant bit has. So if the most significant bit is 1, the shift will fill in 1s. Same for 0s. Filling in the most significant bit preserves the value of the destination when interpreted as a 2s complement integer. If you didn’t know that, you might want to review 2s complement arithmetic. The last shift instruction is shift right logical, which shifts the source 1 register to the right by source 2 bits and always fills with zeroes. The xor instruction does bitwise exclusive-or of the two source operands. This means each bit of source 1 is xored with the bit in the same location in source 2, and the result gets written to the destination. The and does bitwise-and, and the or does bitwise-inclusive or. Noticeably absent is multiplication and division, which are actually not in the base RISC-V instruction set and we may discuss them later. Also missing is a logical NOT instruction. Logical complement of a register can actually be done by XOR’ing it with 0, so a specific instruction for logical NOT is logically not needed.

## Slide 16: Absolute Value by Bit Twiddling
Operator precedence:
Multiplication (*) → Precedence: 3, Left-to-right associativity
Subtraction (-) → Precedence: 4, Left-to-right associativity
Bitwise right shift (>>) → Precedence: 5, Left-to-right associativity
https://en.cppreference.com/w/c/language/operator_precedence
int abs(int v)
{
int mask = v >> 4 * 8 - 1;
return (v + mask) ^ mask;
}
Notes: Remember this example that calculates an absolute value without using a conditional statement? Let’s quickly walk through it again before we look at a version using conditionals.

## Slide 17: Absolute Value by Bit Twiddling
https://en.cppreference.com/w/c/language/operator_precedence
int abs(int v)
{
int mask = v >> 4 * 8 - 1;
return (v + mask) ^ mask;
}
v >> (4 * 8 – 1)
Notes: Remember this example that calculates an absolute value without using a conditional statement? Let’s quickly walk through it again before we look at a version using conditionals.

## Slide 18: Absolute Value by Bit Twiddling
https://en.cppreference.com/w/c/language/operator_precedence
int abs(int v)
{
int mask = v >> 4 * 8 - 1;
return (v + mask) ^ mask;
}
v >> (4 * 8 – 1)
v >> 31
Notes: Remember this example that calculates an absolute value without using a conditional statement? Let’s quickly walk through it again before we look at a version using conditionals.

## Slide 19: Absolute Value by Bit Twiddling
int abs(int v)
{
int mask = v >> 4 * 8 - 1;
return (v + mask) ^ mask;
}
abs: srai t0, a0, 31
add a0, a0, t0
xor a0, a0, t0
ret
Notes: Remember this example that calculates an absolute value without using a conditional statement? Let’s quickly walk through it again before we look at a version using conditionals.

## Slide 20: Absolute Value by Bit Twiddling
int abs(int v)
{
int mask = v >> 4 * 8 - 1;
return (v + mask) ^ mask;
}
abs: srai t0, a0, 31
Notes: The first line of C code becomes one instruction to shift the sign bit through the entire temporary register t0.

## Slide 21: Absolute Value by Bit Twiddling
int abs(int v)
{
int mask = v >> 4 * 8 - 1;
return (v + mask) ^ mask;
}
abs: srai t0, a0, 31
add a0, a0, t0
xor a0, a0, t0
Notes: Then the input parameter is added to the mask before xor’ing with the mask, putting the result in to a0 to return it.

## Slide 22: Absolute Value by Bit Twiddling
int abs(int v)
{
int mask = v >> 4 * 8 - 1;
return (v + mask) ^ mask;
}
abs: srai t0, a0, 31
add a0, a0, t0
xor a0, a0, t0
ret
Notes: The function returns with the return value in a0.

## Slide 23: Absolute Value by Conditional
int abs(int v)
{
return (v < 0) ? –(unsigned int)v : v;
}
Ternary conditional expression evaluates different expressions based on whether the condition (v < 0) is true or false
If v is non-negative, jump to return. If v is negative, compute – v and return.
Notes: Here’s a little more direct way to find an absolute value using a conditional expression. This shows us a few new instructions. Let’s walk through this example.

## Slide 24: Absolute Value by Conditional
int abs(int v)
{
return (v < 0) ? –(unsigned int)v : v;
}
slt t0, a0, zero
beq t0, zero, .L1
sub a0, zero, a0
.L1: ret
Notes: Here’s a little more direct way to find an absolute value using a conditional expression. This shows us a few new instructions. Let’s walk through this example.

## Slide 25: Absolute Value by Conditional
int abs(int v)
{
return (v < 0) ? –(unsigned int)v : v;
}
slt t0, a0, zero // t0 = 1 if a0 < 0, else 0
beq t0, zero, .L1
sub a0, zero, a0
.L1: ret
slt (set less than) instruction sets t0 to 1 if a0 < 0 and 0 otherwise
Notes: The slt mnemonic means set-less-than. This instruction sets the destination register to 1 if src1 is less than src2, and 0 otherwise. We have a direct check here to compare if v is less than 0, that is, if it is negative. So t0 will be set if v is negative, and cleared if v is non-negative. We’ll take a closer look at other ways to use slt after this example.

## Slide 26: Absolute Value by Conditional
int abs(int v)
{
return (v < 0) ? –(unsigned int)v : v;
}
slt t0, a0, zero // t0 = 1 if a0 < 0, else 0
beq t0, zero, .L1 // if a0 is non-negative, return
sub a0, zero, a0
.L1: ret
Notes: Looking at the C code we see it is a ternary operator. If you’re not familiar with this operator, it encodes an if-else condition in one line. The if-block follows the question mark, and the else block follows the colon. So, if v is less than zero the statement should result in the negative unsigned long of v, and if v is greater-than-or-equal to zero the statement should result in v. The condition used in the assembly here is the less-than inequality. We know that we have a zero in t0 if v is non-negative, we can use a branch-if-equal or beq instruction to compare t0 with 0, if the two registers are equal, then the program counter will become the address of the instruction located at the label provided in the branch instruction, here that is L2. Otherwise, if t0 is not zero, then the next instruction in program order will be fetched as usual. This means the program execution will branch if v is negative. From the C code, that means jumping to the code that follows the question mark, which will return the negation of the unsigned cast of v. The branch target is .L2, which is an assembler label that identifies the address of the instruction following the L2 label. If v is not negative, the PC will be advanced to the address of the next straight-line instruction, which is what follows the colon, here just to return v. This instruction happens to also be labeled, but for now the L1 label is ignored.

## Slide 27: Absolute Value by Conditional
int abs(int v)
{
return (v < 0) ? –(unsigned int)v : v;
}
slt t0, a0, zero // t0 = 1 if a0 < 0, else 0
beq t0, zero, .L1 // if v is non-negative, return
sub a0, zero, a0 // if v is negative, do -v
.L1: ret
Notes: Now for the branch-taken case. Jumping to L2 sets the PC to the address of the first instruction in the assembly code after the label. You’ll usually see this written either on the same line as the label, or sometimes the label is written on a line by itself with the instruction on the next line. The label itself does not take up any space in the program. Adding a newline after the label does not change the instruction of the jump target. Anyway, the first instruction after the label uses sub to negate a0, which holds v, putting the result into a0 so it is ready to return. Now a0 holds the positive of v, that is, its absolute value.

## Slide 28: Absolute Value by Conditional
int abs(int v)
{
return (v < 0) ? –(unsigned int)v : v;
}
slt t0, a0, zero // t0 = 1 if a0 < 0, else 0
beq t0, zero, .L1 // if a0 is non-negative, return
sub a0, zero, a0 // if a0 is negative
.L1: ret // return
Notes: Now the execution of ret will return the negation of v, because that was written into a0 by the code at L2.

## Slide 29
Thank you.