## Slide 1: CS 2160 Introduction to Assembly Programming and Computer Organization Lecture 01: Arithmetic
Fall 2026
Instructor: Himon Thakur
TA: Hassan Shakil
University of Colorado Colorado Springs (UCCS)
Himon Thakur (hthakur@uccs.edu); CC BY-NC-SA 4.0;
Special Thanks to Dr. Keith Paarpong and Dr. Xi Tan.

## Slide 2: Today’s Agenda.
- Understand RISC-V basic assembly arithmetic operations
  RV32I: Base Integer Instruction Set, 32-bit
How is a program made?
From source to executable, loading to the computer.
What is a processor?
PC, registers, memory (data, instruction)

## Slide 3: What is RISC-V.
CISC: complex instruction set computing architecture
  For example, x86.
RISC: reduced instruction set computing architecture
  e.g., ARM (smartphones), MIPS (routers), RISC-V (edge computing and AI, embedded systems)
  RISC-V: fifth generation of RISC architecture developed at UC Berkeley.

## Slide 4: RISC-V is a family of Instruction Sets .
Instruction set:
The vocabulary of commands, understood by a given architecture.
Instructions tell the processor what to do
  1 operation
  0+ operands

## Slide 5: RISC-V is a family of Instruction Sets.
Many instruction sets with variants exist
  e.g., RV32I, RV64I, RV128I
We will focus on the RV32I instruction set:
  RV: RISC-V
  32: 32-bit registers
  I: Integer operations

## Slide 6: Registers.
General-purpose registers are storage in the processor
  Typically numbered starting from 0
  Assembly prepends register number with a symbol (x# in RISC-V, $# in MIPS, r# in x86_64). For example, , x0, x1, x2...
  Registers usually have mnemonic names (pc for “program counter”, sp for “stack pointer”)
Processor
PC
Registers
Processor
PC
Registers

## Slide 7: A few RISC-V Integer Registers by mnemonic.
Mnemonic | Meaning
zero | always zero
t0-t6 | temporary registers
a0-a7 | function arguments (a0, a1 also used for return value)
There are 32 general-purpose registers in RISC-V.

## Slide 8: Instructions.
Arithmetic/Logic instructions manipulate register data
Load/store instructions move data in/out of registers
Conditional instructions check values in registers

## Slide 9: Instructions.

## Slide 10: Instructions.

## Slide 11: Instructions.

## Slide 12
Chapter 01: Course Overview

## Slide 13: Let’s do some simple math!
C: High-Level Language
a = b + c;
Assembly: Low-level Language
add a, b, c

## Slide 14: Let’s do some simple math!
Input operands
C: High-Level Language
a = b + c;
Assembly: Low-level Language
add a, b, c
Operation
Output operand

## Slide 15: Let’s do some simple math!
C: High-Level Language
a = b + c;
Assembly: Low-level Language
add a, b, c
Where are a, b, c?
We need to know more context.

## Slide 16: Let’s do some simple math!
C: High-Level Language
a = b + c;
Assembly – RISC-V
add a, b, c
add t1, a0, a1
Where are a, b, c?
For now, we’ll just make assumptions:
  b is in register a0 c is in register a1 a goes in register t1

## Slide 17: Let’s do subtraction!
C: High-Level Language
d = e - f;
Assembly
sub d, e, f

## Slide 18: Let’s do subtraction!
C: High-Level Language
d = e - f;
Assembly – RISC V
sub a1, t0, t5
Assume:
  e is in register t0 f is in register t5 d goes in register a1

## Slide 19: Let’s multiply by a power of 2!
C: High-Level Language
g = h * 256;
Assembly
mul g, h, 256

## Slide 20: Let’s multiply by a power of 2!
C: High-Level Language
g = h * 256;
Assembly
mul g, h, 256
RISC-V base integer instruction set (RV32I) does not have a multiply instruction!

## Slide 21: Let’s multiply by a power of 2!
C: High-Level Language
g = h * 256;
Assembly
mul g, h, 256
Multiplication by 2x is equivalent to shifting left by log2(2x)

## Slide 22: Memorize powers-of-2 and log2 up to 1024!
2 = 21
4 = 22
8 = 23
16 = 24
32 = 25
64 = 26
128 = 27
256 = 28
512 = 29
1024 = 210
Combine with SI prefixes for larger numbers.
Notes: Draw figures on the whiteboard to explain why shift works

## Slide 23: Multiplication
Multiplication by 2x is equivalent to shifting left by log2(x)
Example:
Multiplication by 8
  8 = 23
  so log2(8) = 3
  To multiply a number by 8, shift it left by 3 positions
Example with 6 (binary: 110):
  Multiply by 8: 6 * 8 = 48
  Left shift 110 by 3: 110000 (binary for 48)
Notes: Draw figures on the whiteboard to explain why shift works

## Slide 24: Let’s multiply by a power of 2!
High-Level Language – C
g = h * 256;
Assembly – RISC-V
mul g, h, 256
slli g, h, 8
Multiplication by 28 is equivalent to shifting left by log2(28) = 8

## Slide 25: Let’s multiply by a power of 2!
High-Level Language – C
g = h * 256;
Assembly – RISC-V
mul g, h, 256
slli g, h, 8
slli t4, t3, 8
Assume h is in t3, g goes in t4

## Slide 26: Multiplication by other numbers.
High-Level Language – C
g = h * 18;
Assembly
mul g, h, 18

## Slide 27: Multiplication by other numbers.
High-Level Language – C
g = h * 18;
Assembly
mul g, h, 18
h*18 = h*16 + h*2

## Slide 28: Multiplication by other numbers.
High-Level Language – C
g = h * 18;
Assembly
mul tmp1, h, 16
mul tmp2, h, 2
add g, tmp1, tmp2
h * 16
h*18 = h*16 + h*2
h * 2

## Slide 29: Multiplication by other numbers.
High-Level Language – C
g = h * 18;
Assembly – RISC-V
mul tmp1, h, 16
slli tmp1, h, 4
mul tmp2, h, 2
slli tmp2, h, 1
add g, tmp1, tmp2

## Slide 30: Multiplication by other numbers.
High-Level Language – C
g = h * 18;
Assembly – RISC-V
mul tmp1, h, 16
slli t0, t3, 4
mul tmp2, h, 2
slli t1, t3, 1
add t4, t0, t1
Assume h is in t3, g goes in t4, t0 and t1 available to use

## Slide 31: Multiplication by other numbers.
High-Level Language – C
g = h * 18;
Assembly – RISC-V
mul tmp1, h, 16
slli t0, t4, t3, 4
mul tmp2, h, 2
slli t1, t3, 1
add t4, t0, t4, t1
Can be done using one less temporary register by re-using t4 for the intermediate output.

## Slide 32: Let’s do some simple math!
Category | Instruction | Example | Meaning | Comments
Arithmetic | Add | add x5. x6. x7 | X5 = x6 = x7 | Three register operands; add
 | Subtract | sub x5. x6. x7 | X5 = x6 – x7 | Three register operands; subtract
 | Add immediate | addi x5. x6. 20 | X5 = x6 + 20 | Used to add constants
Refer to Book Figure 2.1 for more info

## Slide 33: Let’s do some simple math!
Operation | Format | Computation | 
addition | add | dest, src1, src2 | dest = src1 + src2
subtraction | sub | dest, src1, src2 | dest = src1 - src2
shift left | sll | dest, src1, src2 | dest = src1 << src2
Refer to Book Figure 2.1 for more info
  Also available with immediate versions (except sub):
    addi dest, src1, imm dest = src1 + Imm
    slli dest, src1, imm dest = src1 << Imm

## Slide 34: Arithmetic Expression Example.
Carnegie Mellon
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 + t5;
return rval;
}
arith:
add t1, a0, a1
add t2, a2, t1
add t4, a1, a1
add t4, t4, a1
slli t4, t4, 4
add t5, a0, t4
add a0, t2, t5
ret
Notes: Let’s put some of these instructions into context with a contrived example. Here’s a function that takes three 32-bit integer arguments, x y and z. It then calculates several arithmetic expressions, eventually returning (x+y+z) + (x + y*48). Here is one way to generate assembly for this function. We can see several interesting instructions. Let’s break it down.

## Slide 35: Arithmetic Expression Example.
Carnegie Mellon
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 + t5;
return rval;
}
arith:
add t1, a0, a1
add t2, a2, t1
add t4, a1, a1
add t4, t4, a1
slli t4, t4, 4
add t5, a0, t4
add a0, t2, t5
ret
Register | Use(s)
a0 | Argument x
a1 | Argument y
a2 | Argument z
Notes: Let’s put some of these instructions into context with a contrived example. Here’s a function that takes three 32-bit integer arguments, x y and z. It then calculates several arithmetic expressions, eventually returning (x+y+z) + (x + y*48). Here is one way to generate assembly for this function. We can see several interesting instructions. Let’s break it down.

## Slide 36: Arithmetic Expression Example.
Carnegie Mellon
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 + t5;
return rval;
}
arith:
add t1, a0, a1
add t2, a2, t1
add t4, a1, a1
add t4, t4, a1
slli t4, t4, 4
add t5, a0, t4
add a0, t2, t5
ret
Register | Use(s)
a0 | Argument x
a1 | Argument y
a2 | Argument z
Notes: Let’s put some of these instructions into context with a contrived example. Here’s a function that takes three 32-bit integer arguments, x y and z. It then calculates several arithmetic expressions, eventually returning (x+y+z) + (x + y*48). Here is one way to generate assembly for this function. We can see several interesting instructions. Let’s break it down.

## Slide 37: Arithmetic Expression Example.
Carnegie Mellon
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 + t5;
return rval;
}
arith:
add t1, a0, a1
add t2, a2, t1
add t4, a1, a1
add t4, t4, a1
slli t4, t4, 4
add t5, a0, t4
add a0, t2, t5
ret
Register | Use(s)
a0 | Argument x
a1 | Argument y
a2 | Argument z
Notes: Let’s put some of these instructions into context with a contrived example. Here’s a function that takes three 32-bit integer arguments, x y and z. It then calculates several arithmetic expressions, eventually returning (x+y+z) + (x + y*48). Here is one way to generate assembly for this function. We can see several interesting instructions. Let’s break it down.

## Slide 38: Arithmetic Expression Example.
Carnegie Mellon
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x;
int t4 = y * 48;
int t5 = x + t4;
int rval = t2 + t5;
return rval;
}
arith:
add t1, a0, a1
add t2, a2, t1
add t4, a1, a1
add t4, t4, a1
slli t4, t4, 4
add t5, a0, t4
add a0, t2, t5
ret
Register | Use(s)
a0 | Argument x
a1 | Argument y
a2 | Argument z
Notes: Let’s put some of these instructions into context with a contrived example. Here’s a function that takes three 32-bit integer arguments, x y and z. It then calculates several arithmetic expressions, eventually returning (x+y+z) + (x + y*48). Here is one way to generate assembly for this function. We can see several interesting instructions. Let’s break it down.

## Slide 39: Arithmetic Expression Example.
Carnegie Mellon
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x;
int t4 = y * 48;
int t5 = x + t4;
int rval = t2 + t5;
return rval;
}
arith:
add t1, a0, a1
add t2, a2, t1
add t4, a1, a1
add t4, t4, a1
slli t4, t4, 4
add t5, a0, t4
add a0, t2, t5
ret
Register | Use(s)
a0 | Argument x
a1 | Argument y
a2 | Argument z
Notes: Let’s put some of these instructions into context with a contrived example. Here’s a function that takes three 32-bit integer arguments, x y and z. It then calculates several arithmetic expressions, eventually returning (x+y+z) + (x + y*48). Here is one way to generate assembly for this function. We can see several interesting instructions. Let’s break it down.

## Slide 40: Arithmetic Expression Example.
Carnegie Mellon
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x;
int t4 = y * 48;
int t5 = x + t4;
int rval = t2 + t5;
return rval;
}
arith:
add t1, a0, a1
add t2, a2, t1
add t4, a1, a1
add t4, t4, a1
slli t4, t4, 4
add t5, a0, t4
add a0, t2, t5
ret
Register | Use(s)
a0 | Argument x
a1 | Argument y
a2 | Argument z
Notes: Let’s put some of these instructions into context with a contrived example. Here’s a function that takes three 32-bit integer arguments, x y and z. It then calculates several arithmetic expressions, eventually returning (x+y+z) + (x + y*48). Here is one way to generate assembly for this function. We can see several interesting instructions. Let’s break it down.

## Slide 41: Arithmetic Expression Example.
Carnegie Mellon
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x;
int t4 = y * 48;
int t5 = x + t4;
int rval = t2 + t5;
return rval;
}
arith:
add t1, a0, a1
add t2, a2, t1
add t4, a1, a1
add t4, t4, a1
slli t4, t4, 4
add t5, a0, t4
add a0, t2, t5
ret
Register | Use(s)
a0 | rval
a1 | Argument y
a2 | Argument z
Notes: Let’s put some of these instructions into context with a contrived example. Here’s a function that takes three 32-bit integer arguments, x y and z. It then calculates several arithmetic expressions, eventually returning (x+y+z) + (x + y*48). Here is one way to generate assembly for this function. We can see several interesting instructions. Let’s break it down.

## Slide 42: Arithmetic Expression Example.
Carnegie Mellon
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x;
int t4 = y * 48;
int t5 = x + t4;
int rval = t2 + t5;
return rval;
}
arith:
add t1, a0, a1
add t2, a2, t1
add t4, a1, a1
add t4, t4, a1
slli t4, t4, 4
add t5, a0, t4
add a0, t2, t5
ret
Register | Use(s)
a0 | Argument x
a1 | Argument y
a2 | Argument z
Notes: Let’s put some of these instructions into context with a contrived example. Here’s a function that takes three 32-bit integer arguments, x y and z. It then calculates several arithmetic expressions, eventually returning (x+y+z) + (x + y*48). Here is one way to generate assembly for this function. We can see several interesting instructions. Let’s break it down.

## Slide 43: Exercise: Convert to RISC-V.
Reminders:
  a in a0, b in a1
  Put return value in a0
  Can use temporary registers t0-t7
int silly_math(int a, int b)
{
int k = (b – a) + 11;
return k*42;
}

## Slide 44: Exercise solution.
silly_math:
sub t0, a1, a0 # (b-a)
addi t0, t0, 11 # (b-a)+11
slli t1, t0, 2 # 4*k
add t1, t1, t0 # 4*k+k
slli t1, t1, 2 # 4(4*k+k)
add t1, t1, t0 # 4(4k+k)+k
slli a0, t1, 1
ret
int= silly_math(int a, int b)
{
int k = (b – a) + 11;
return k*42;
}
k*42 = k*(32+8+2) = 2*( 4*(4k+1k)+1k)

## Slide 45: Summary.
Things you should know or go learn more about:
  RISC-V assembly programming straight-line code with basic arithmetic
    Addition, subtraction, multiplication (shifts and adds)
  Basic function call/return
    Function calls that don’t make nested function calls (leaf procedures)
Next up: basic data movement
Read chapter 2!

## Slide 46
Thank you.