## Slide 1: CS 2160 Introduction to Assembly Programming and Computer Organization Lecture 03: Branching, Procedures, and Loops
Fall 2026
Instructor: Himon Thakur
TA: Hassan Shakil
University of Colorado Colorado Springs (UCCS)
Himon Thakur (hthakur@uccs.edu); CC BY-NC-SA 4.0;
Special Thanks to Dr. Keith Paarpong and Dr. Xi Tan.

## Slide 2: Today’s Agenda.
Understand RISC-V basic assembly control flow and conditional statements.
Instructions for making decisions
Conditional statements: If, else structures
Loops: while, do while, for

## Slide 3: Instructions for Making Decisions (§2.7)
Decisions are important for:
choosing between alternatives (found in conditional statements)
iterating a computation (found in loops)
The same assembly instructions are the building blocks for both cases

## Slide 4: Instructions for Making Decisions (§2.7)
Branch instructions
Commonly represented by an if statement, combined with go to statement
> beq rs1, rs2, Label
Go to statement Label if the value in register rs1 equals value in register rs2.
> bne rs1, rs2, Label
Go to statement Label if the value in register rs1 is not equal value in register rs2.
> blt rs1, rs2, Label
Go to statement Label if the value in register s1 is less than value in register s2.
> bge rs1, rs2, Label
Go to statement called Label if the value in register s1 is greater or equal than value in register s2.

## Slide 5
t2 | h
t1 | g
t3 | i
t4 | j
Registers
t0 | f
C Code
if(i == j){ f = g + h;
}
else{
f = g - h;
}
Example: if else conditional branching.

## Slide 6: Example: if else conditional branching.
if (i==j) goto Then; f = g - h;
Then:
f = g + h; Exit:
if (i!=j) goto Else; f = g + h;
Else:
f = g - h; Exit:
C Code: goto version 2
if(i == j){ f = g + h;
}
else{
f = g - h;
}
Example: if else conditional branching.
Example: if else conditional branching.
C Code: goto version 1
C Code

## Slide 7: Example: if else conditional branching.
if(i == j){ f = g + h;
}
else{
f = g - h;
}
t2 | h
t1 | g
t3 | i
t4 | j
Registers
t0 | f
bne t3, t4, Else add t0, t1, t2 beq x0, x0, Exit Else:
sub t0, t1, t2 Exit:
beq t3, t4, Then sub t0, t1, t2 beq x0, x0, Exit Then:
add t0, t1, t2 Exit:
Assembly code version 1
Assembly code version 2
C Code

## Slide 8: If else conditional branching template.
if(cond){
body_if
}
else{
body_else
}
if(!cond)goto Else
body_if
goto Exit Else:
body_else
Exit:
body: {
statement1; statement2;
…
}
if(cond)goto If
body_else
goto Exit If:
body_if
Exit:
Assembly code template 1
Assembly code template 2
C Code

## Slide 9: Example: if else.
10
C Code
int abs(int v)
{
int r;
if (v < 0)
r = -v;
else
r = v; return r;
}

## Slide 10: Example: if else.
10
C Code
int abs(int v)
{
int r;
if (v < 0)
r = -v;
else
r = v; return r;
}
int abs(int v)
{
int r;
int cond = v < 0;
if (cond) goto Then; r = v;
goto Done; Then:
r = -v; Done:
return r;
}
C Code: : goto version

## Slide 11: Example: if else.
10
C Code
int abs(int v)
{
int r;
if (v < 0)
r = -v;
else
r = v; return r;
}
int abs(int v)
{
int r;
int cond = v < 0;
if (cond) goto Then; r = v;
goto Done; Then:
r = -v; Done:
return r;
}
C Code: : goto version
abs:
slt t0, a0, x0 bne t0, x0, Then j Exit
Then:
sub a0, x0, a0 Exit:
ret
Assembly Code

## Slide 12: Example: while.
while(A[i] == k){ i += 1;
}
a2 | &A[0]
Registers
a0 | i
a1 | k
t0 | 
C Code
Exercise

## Slide 13: Example solution: while.
while(A[i] == k){ i += 1;
}
a2 | &A[0]
Registers
a0 | i
a1 | k
t0 | 
C Code
Loop:
slli |  | t0, | a0, | 2 | // | t0 | = | i*4
add t0, t0, a2 |  |  |  |  | // | t0 | = | &A[i]
lw t1, 0(t0) |  |  |  |  | // | t1 | = | A[i]
bne t1, a1, Exit addi a0, a0, 1 |  |  |  |  | // // | A[i] != k i = i + 1 |  | 
beq x0, x0, Loop |  |  |  |  | // | go to Loop |  | 
Exit:
Assembly Code (Example 2.6 in book

## Slide 14: General 'while' template #1.
C Code
goto version
Loop:
if (!Cond)goto Exit;
Body
goto Loop; Exit:
while (Cond)
Body

## Slide 15: General 'while' template #1.
C Code
goto version
Loop:
if (!Cond)goto Exit;
Body
goto Loop; Exit:
while (Cond)
Body
Loop:
slli t0, a0, 2
add t0, t0, a2 | // | t0 | = | &A[i]
lw t1, 0(t0) | // | t1 | = | A[i]
bne t1, a1, Exit addi a0, a0, 1
beq x0, x0, Loop Exit:
Assembly code
{

## Slide 16: General 'while' template #2.
C Code
goto version
goto Test; Loop:
Body
Test:
if (Cond)goto Loop; Exit:
while (Cond)
Body
"Jump-to-middle" translation​

## Slide 17: General 'while' template #2.
C Code
goto version
goto Test; Loop:
Body
Test:
if (Cond)goto Loop; Exit:
while (Cond)
Body
Assembly code
// i = i + 1
beq x0, x0, Test Loop:
addi a0, a0, 1 Test:
slli t0, a0, 2
add t0, t0, a2 lw t1, 0(t0)
beq t1, a1, Loop
// t0 = i*4
// t0 = &A[i]
// t1 = A[i]
// A[i] == k
Exit:
{
// i = i + 1
beq x0, x0, Test Loop:
addi a0, a0, 1 Test:
slli t0, a0, 2
add t0, t0, a2 lw t1, 0(t0)
beq t1, a1, Loop
// t0 = i*4
// t0 = &A[i]
// t1 = A[i]
// A[i] == k
Exit:
{
"Jump-to-middle" translation​

## Slide 18: While loop: example #2
int pcount_while(unsigned int x) {
int result = 0; while (x) {
result += x & 1; x >>= 1;
}
return result;
}
int pcount_goto_jtm(unsigned int x) {
int result = 0; goto test;
loop:
result += x & 1; x >>= 1;
test:
if(x) goto loop; return result;
}
Count number of 1’s in argument x ('popcount')
C Code
goto version (template 2)

## Slide 19: While loop: example #2
21
int pcount_goto_jtm(unsigned int x) {
int result = 0; goto test;
Loop:
result += x & 1; x >>= 1;
Test:
if(x) goto Loop; return result;
}
addi t0, x0, 0 beq x0, x0, Test
Loop:
andi t1, x0, 1 // x & 1
add t0, t0, t1 // result += t srli a0, a0, 1 // x >>= 1
Test:
bne x0, a0, Loop
addi a0, t0, 0 // return Exit:
Count number of 1’s in argument x ('popcount')
goto version (template 2)
Assembly code

## Slide 20
22
C Code
do
body
while (COND);
Goto Version
loop:
body
if (COND)
goto loop
General 'do-while' template.

## Slide 21
C Code
int pcount_do (unsigned int x)
{
int result = 0; do {
result += x & 1; x >>= 1;
} while (x); return result;
}
Goto Version
int pcount_goto (unsigned int x)
{
int result = 0; loop:
result += x & 1; x >>= 1;
if(x) goto loop; return result;
}
'do-while' for the previous example.
Count number of 1’s in argument x ('popcount')

## Slide 22
24
addi | t0, | zero, |  | 0 | # |  |  | result = |  |  |  |  |  | 0
Loop: andi | t1, | a0, | 1 | # |  | # loop: t = x & |  |  |  |  | 0x1 |  |  | 
add | t0, | t0, | t1 |  | # |  |  | result |  |  |  |  | += t | 
srli | a0, | a0, | 1 |  | # | x >>= |  |  |  | 1 |  |  |  | 
bne | a0, | x0, | Loop |  | # |  | if |  | (x) |  |  | goto |  | loop
addi | a0, | t0, | 0 | # | return |  |  |  | result |  |  |  |  | 
ret |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Goto Version Assembly code
int pcount_goto (unsigned int x)
{
int result = 0; loop:
result += x & 1; x >>= 1;
if(x) goto loop; return result;
}
'do-while' loop compilation.

## Slide 23
25
#define WSIZE 8*sizeof(int) int pcount_for
(unsigned int x)
{
size_t i; int r;
for (r = 0, i = 0;
i < WSIZE; i++)
{
r += (x >> i) & 1;
}
return r;
}
r = 0, i = 0
i < WSIZE
i++
{
r += (x >> i) & 1;
}
Init
Cond
Update
Body
for(Init;Cond;Update)
Body
'for' loop template.

## Slide 24
Init;
while (Cond ) {
Body
Update;
}
While loop version
for(Init;Cond;Update)
Body
for loop version
'for' loop  'while' loop conversion.

## Slide 25
int pcount_for_while (unsigned int x)
{
size_t i; int r;
r = 0, i = 0;
while (i < WSIZE)
{
r += (x >> i) & 1; i++;
}
return r;
}
r = 0,i =0
i < WSIZE
i++
{
r += (x >> i) & 1;
}
for-while loop conversion.
Init
Cond
Update
Body

## Slide 26
main()
func1a(..)
func1b(..)
func2a(..)
func2b(..)
func2c(..)
func2d(..)
leafa(..)
leafb(..)
leafn(..)
Nested procedures.

## Slide 27
29
func2a(..)
c2d(..)
nc1a(..) func1b(..)
func2b(..) func2c(..) fun
leafa(..)
leafb(..)
leafn(..)
main()
fu Multiple procedure calls will eventually conflict with register values.
Need to use the stack to preserve data
return address
Saved variables
Nested procedures.

## Slide 28
Block of memory used by compiler as a stack data structure
The stack “grows down”
Register sp contains the “lowest” stack address
Points to the “top” element
Stack Pointer:
sp
Increasing Addresses
Stack “Top”
Stack “Bottom”
Decreasing Addresses
RISC-V stack.

## Slide 29
rs1
rs2
Increasing Addresses
Stack “Top”
Decreasing Addresses
Stack “Bottom”
addi sp, sp, -8
Decrement sp by 8 to make room on the stack
sw rs1, 4(sp)
sw rs2, 0(sp)
New stack pointer sp
Old stack pointer
RISC-V stack.

## Slide 30
rs1
rs2
Increasing Addresses
Stack “Top”
Stack “Bottom”
Decreasing Addresses
New stack pointer sp
Old stack pointer
lw dst2, 0(sp) lw dst1, 4(sp)
pop stack from the top
addi sp, sp, 8
Deallocate 8 bytes from top
RISC-V stack.

## Slide 31
-4
Stack Grows Down
Increasing Addresses
Stack “Bottom”
Prev Stack Pointer: sp
Next Stack Pointer: sp
Stack “Top”
lw | dst1, | 0(sp)
lw | dst2, | 0(sp)
addi
sp, sp, -8
Allocating and pushing to the stack.

## Slide 32
Stack Grows Down
Increasing Addresses
Stack “Top”
Stack “Bottom”
lw Dst, 0(sp)
Read value from top of stack at 0(sp)
This is optional in RISC-V (and most RISC ISAs)
addi sp, sp, 4
Deallocate 4 bytes from the top of the stack
+4
Next Stack Pointer: sp
Prev Stack Pointer: sp
Popping and freeing from the stack.

## Slide 33
int caller () {
return absadd(-1, 2);
}
int absadd (int x, int y) { int t0 = abs(x);
int t1 = abs(y) return t0+t1;
}
int abs (int v) {
int mask = v >> 4 * 8 - 1; return (v + mask) ^ mask;
}
Procedure control-flow: example.

## Slide 34
caller:
400500: | addi | sp, | sp, -4 |  |  | 
400504: | sw | ra, | 0(sp) | # | save | ret addr
400508: | addi | a0, | x0, -1 | # | arg0 | = -1
40050C: | addi | a1, | x0, 2 | # | arg1 | = 2
400510: jal
400514: lw
400518: jalr
ra, absadd ra, 0(sp) x0, ra
# absadd(-1,2) # restore ra
# return
int abs (int v) {
int mask = v >> 4 * 8 - 1; return (v + mask) ^ mask;
}
int absadd (int x, int y) { int t0 = abs(x);
int t1 = abs(y) return t0+t1;
}
int caller () {
return absadd(-1, 2);
}
Procedure control-flow: example.

## Slide 35
absadd: 400540: addi
400544: sw
400548: sw
40054C: sw
sp, sp, -12
ra, 8(sp)
s0, 4(sp)
a1, 0(sp)
# Allocate stack # Save ret addr # Save s0 reg
# Save y
40055C: | jal | ra, | abs | # | abs(x)
400560: | add | s0, | a0, x0 | # | s0 = abs(x)
400558: | lw | a0, | 0(sp) | # | a0 = y
40055C: | jal | ra, | abs | # | abs(y)
400560: | add | a0, | a0, s0 | # | a0 = ¦x¦+¦y¦
400564: | lw | s0, | 4(sp) | # | Restore s0 reg
400568: | lw | ra, | 8(sp) | # | Restore ret
addr
40056C: addi 400570: jalr
sp, sp, 12 x0, ra
# Free stack # ret
int abs (int v) {
int mask = v >> 4 * 8 - 1; return (v + mask) ^ mask;
}
int absadd (int x, int y) { int t0 = abs(x);
int t1 = abs(y) return t0+t1;
}
int caller () {
return absadd(-1, 2);
}
Procedure control-flow: example.

## Slide 36
int abs (int v) {
int mask = v >> 4 * 8 - 1; return (v + mask) ^ mask;
}
int absadd (int x, int y) { int t0 = abs(x);
int t1 = abs(y) return t0+t1;
}
abs:
400570: sra
400574: add
400578: xor 40057C: jalr
t0, a0, 31
a0, a0, t0 a0, a0, t0 x0, ra
# mask = v >> 31 # v + m
# a0=(v + m) ^ m # return a0
int caller () {
return absadd(-1, 2);
}
Procedure control-flow: example.

## Slide 37
absadd: 400540: addi
400544: sw
sp, sp, -12
ra, 8(sp)
•
•
40055C: jal
•
•
400568: lw
40056C: addi 400570: jalr
ra, abs
ra, 8(sp) sp, sp, 12 x0, ra
0x400510
0x11C
•
•
•
sp
0x120
0x11C
0x118
0x114
0x110
pc
ra
caller:
•
•
400510: jal ra, absadd
400514: lw ra, 0(sp)
•
•
0x400514
A closer look.

## Slide 38
400540: addi sp, sp, -12
absadd:
400544: sw ra, 8(sp)
•
•
40055C: jal
•
•
400568: lw
40056C: addi 400570: jalr
ra, abs
ra, 8(sp) sp, sp, 12 x0, ra
Caller:
•
•
400510: jal
400514: lw
ra, absadd ra, 0(sp)
•
•
0x400540
pc
0x400514
ra
0x110
sp
•
•
•
0x120
0x11C
0x118
0x114
0x110
A closer look.

## Slide 39
absadd:
400540: addi sp, sp, -12
400544: sw ra, 8(sp)
•
•
40055C: jal
ra, abs
•
•
400568: lw
40056C: addi 400570: jalr
ra, 8(sp) sp, sp, 12 x0, ra
caller:
•
•
400510: jal
400514: lw
ra, absadd ra, 0(sp)
•
•
0x400544
0x110
sp
pc
0x400514
ra
0x120
0x11C
0x118
0x114
0x110
•
•
•
00400514
A closer look.

## Slide 40
absadd: 400540: addi
400544: sw
sp, sp, -12
ra, 8(sp)
•
•
40055C: jal ra, abs
•
•
400568: lw
40056C: addi 400570: jalr
ra, 8(sp) sp, sp, 12 x0, ra
caller:
•
•
400510: jal
400514: lw
ra, absadd ra, 0(sp)
•
•
•
•
•
00400514
•
•
0x40055C
0x110
sp
pc
ra
0x120
0x11C
0x118
0x114
0x110
0x400560
A closer look.

## Slide 41
absadd: 400540: addi
400544: sw
sp, sp, -12
ra, 8(sp)
•
•
40055C: jal
ra, abs
•
•
400568: lw ra, 8(sp)
40056C: addi 400570: jalr
sp, sp, 12 x0, ra
caller:
•
•
400510: jal
400514: lw
ra, absadd ra, 0(sp)
•
•
0x400568
0x110
sp
pc
ra
•
•
•
00400514
•
•
0x120
0x11C
0x118
0x114
0x110
0x400514
A closer look.

## Slide 42
absadd: 400540: addi
400544: sw
sp, sp, -12
ra, 8(sp)
•
•
40055C: jal
•
•
400568: lw
ra, abs
ra, 8(sp)
40056C: addi sp, sp, 12
400570: jalr x0, ra
caller:
•
•
400510: jal
400514: lw
ra, absadd ra, 0(sp)
•
•
0x40056C
sp
pc
0x400514
ra
•
•
•
00400514
•
•
0x120
0x11C
0x118
0x114
0x110
0x11C
A closer look.

## Slide 43
absadd: 400540: addi
400544: sw
sp, sp, -12
ra, 8(sp)
•
•
40055C: jal
•
•
400568: lw
40056C: addi
ra, abs
ra, 8(sp) sp, sp, 12
400570: jalr x0, ra
caller:
•
•
400510: jal
400514: lw
ra, absadd ra, 0(sp)
•
•
•
•
•
00400514
•
•
0x400570
0x11C
sp
pc
0x400514
ra
0x120
0x11C
0x118
0x114
0x110
A closer look.

## Slide 44
Things you should know or go learn more about:
  RISC-V assembly programming straight-line code with basic arithmetic
    Addition, subtraction, multiplication (shifts and adds)
  Basic function call/return
    Function calls that don’t make nested function calls (leaf procedures)
Next up: Logical operations.
Read chapter 2!
Summery.

## Slide 45
Thank you.